## Slide 1
JU RESEARCH • SIMPLE ARCHITECTURE EXPLANATION
AI Math Engine +
Neural Network Engine
A 32-bit RISC-V SoC where the neural engine predicts and the AI Engine solves or refines complex mathematics in hardware.
NEWTON FIRST
≈30 SOLVERS TARGET
HARDWARE INNER LOOP
NEURAL NETWORK
ENGINE
fast prediction x₀
SHARED MEMORY
result buffer
AI ENGINE
Newton + future solver library
prediction
job data
The whole solver subsystem is your AI Engine.
Newton is Solver 1 inside it; the Neural Network Engine is a separate peer accelerator.
JU RESEARCH • 32-BIT RISC-V • HARDWARE AI MATH ENGINE
01 / 8
Notes: Presenter notes:
- Begin with the naming: AI Engine means the complete mathematical-solver subsystem, not only Newton.
- The Neural Network Engine is a separate compute block that can supply an initial estimate to the AI Engine.
[Sources]
- User-provided JU project requirements and architecture discussion, 22 August 2026.
[/Sources]

## Slide 2
Two engines do different jobs—and work together
SYSTEM VIEW
JU RESEARCH • 32-BIT RISC-V • HARDWARE AI MATH ENGINE
02 / 8
32-bit RISC-V
software + system control
AXI4 SoC Interconnect
NEURAL NETWORK ENGINE
GEMM • convolution • activation
AI ENGINE
Newton + approximately 30 solvers
I/O
sensors • PCIe • Ethernet
SHARED SRAM / DDR
AXI4-Lite
optional AXI-Stream
V1 recommendation: exchange through shared memory; add direct streaming only after the basic system works.
CONTROL / AXI4-Lite
DATA + ADDRESS / AXI4
INTERRUPT / EVENT
OPTIONAL STREAM
Notes: Presenter notes:
- RISC-V configures both accelerators but does not calculate every Newton step.
- AXI4-Lite carries control registers; AXI4 carries bulk tensors, vectors, matrices and addresses.
- Shared memory is the cleanest first connection between the Neural Network Engine and AI Engine.
[Sources]
- User-provided architecture screenshots, 22 August 2026.
- Arm AMBA architecture overview: https://developer.arm.com/Architectures/AMBA
- RISC-V RV32 ISA reference: https://docs.riscv.org/reference/isa/unpriv/rv32.html
[/Sources]

## Slide 3
The neural engine predicts; the AI Engine refines
WORKING TOGETHER
JU RESEARCH • 32-BIT RISC-V • HARDWARE AI MATH ENGINE
03 / 8
1 NEURAL ENGINE
produce a fast estimate
2 SHARED BUFFER
store x₀ + confidence
3 AI ENGINE
select Newton and iterate
4 FINAL RESULT
accurate refined x*
prediction / initial x₀
job data
optimized x*
Example: 10-variable pose refinement
Neural output
x₀ = [position, rotation, scale, …]
Newton hardware
evaluate g/H → solve direction → line search → repeat
Output
x*
more accurate
The AI Engine complements the neural network; it does not replace neural inference.
Notes: Presenter notes:
- Use a real application example: the neural network gives a fast approximate pose; Newton refines a small 6–10 variable state.
- A full Hessian for millions of neural-network weights is generally not the intended V1 use case.
[Sources]
- User-provided JU project requirements and architecture discussion, 22 August 2026.
[/Sources]

## Slide 4
One job moves through hardware without CPU arithmetic
JOB FLOW
JU RESEARCH • 32-BIT RISC-V • HARDWARE AI MATH ENGINE
04 / 8
RV32
NN ENGINE
SHARED MEMORY
AI ENGINE
1 configure + start
2 write prediction x₀
3 NN completion interrupt
4 write AI job descriptor
5 ring AI doorbell
6 read x₀ + equation data
7 write optimized x*
8 AI completion interrupt
Newton loop stays in hardware
CONTROL / AXI4-Lite
DATA + ADDRESS / AXI4
INTERRUPT / EVENT
OPTIONAL STREAM
Notes: Presenter notes:
- The processor performs one setup transaction, not one transaction per Newton arithmetic operation.
- After the doorbell, the AI Engine owns the iterative loop until completion or a defined fault.
- For a non-coherent first implementation, software must manage cache flush/invalidate around shared buffers.
[Sources]
- User-provided JU project requirements and architecture discussion, 22 August 2026.
[/Sources]

## Slide 5
Inside the AI Engine, control selects the solver
AI ENGINE
JU RESEARCH • 32-BIT RISC-V • HARDWARE AI MATH ENGINE
05 / 8
JOB DESCRIPTOR QUEUE
solver_id • N • pointers • limits
DISPATCHER
validate + select solver
SOLVER CONTROL STORE
Newton V1 • LM • CG • BFGS • …
SELECTED SOLVER FSM
Newton controller first
SHARED COMPUTE FABRIC
Equation + derivative
evaluator
2-lane vector / FMA
engine
Matrix factorization +
linear solve
Divider + line search +
convergence
LOCAL SRAM
x • g • H • p • constants • temporary values
RESULT + STATUS
x* • iterations • reason code
kernel issue
CONTROL PATH
chooses the algorithm and schedules kernels
DATA PATH
moves operands through shared arithmetic and SRAM
Notes: Presenter notes:
- The target is about 30 solver modes, but Newton is the first implemented control personality.
- Expensive arithmetic is shared so 30 solvers do not require 30 duplicated datapaths.
- A future Newton hard macro can replace or harden the hottest shared blocks after RTL measurements.
[Sources]
- User-provided JU project requirements and architecture discussion, 22 August 2026.
[/Sources]

## Slide 6
Newton runs as a closed hardware loop
NEWTON SOLVER 1
JU RESEARCH • 32-BIT RISC-V • HARDWARE AI MATH ENGINE
06 / 8
1 LOAD
xₖ + constants
2 EVALUATE
f • gradient g • Hessian H
3 STOP?
small gradient / limit
4 SOLVE
(H + λI)p = −g
5 LINE SEARCH
select α
6 UPDATE + STORE TRIAL
xₖ₊₁ = xₖ + αp
CONVERGED RESULT
x* + status + interrupt
NO
YES
What stays entirely in hardware
iteration counter • regularization λ • factorization • direction solve • line-search trials • convergence checks
Never calculate H⁻¹ explicitly—factor and solve the linear system.
Notes: Presenter notes:
- This is the Newton Solver 1 FSM at the algorithm level.
- The loop continues internally; the CPU is not involved between iterations.
- Regularization and line search improve robustness when the Hessian is unsafe or the full step increases the cost.
[Sources]
- User-provided JU project requirements and architecture discussion, 22 August 2026.
[/Sources]

## Slide 7
Two hardware lanes can process any N one pair at a time
N-VARIABLE MAPPING
JU RESEARCH • 32-BIT RISC-V • HARDWARE AI MATH ENGINE
07 / 8
Example: N = 10 variables, LANES = 2
All values belong to one coupled Newton problem.
x0
x1
x2
x3
x4
x5
x6
x7
x8
x9
full x(k) stored in local SRAM
CYCLE
LANE 0
LANE 1
C0
x0
x1
C1
x2
x3
C2
x4
x5
C3
x6
x7
C4
x8
x9
A Freeze x(k)
B Sweep all vector +
Hessian elements
C Factor and solve the
full 10 × 10 system
D Write all x(k+1),
then swap banks
Do not solve five independent 2-variable problems unless H is block diagonal. Cross-terms couple x₀…x₉.
Notes: Presenter notes:
- The two-variable prototype should become a two-lane reusable datapath.
- For N=10, five lane cycles cover one vector pass, but the complete gradient, Hessian and direction belong to the same iteration.
- Use current and trial x banks; commit the trial bank only after all N values are ready.
[Sources]
- User-provided JU project requirements and architecture discussion, 22 August 2026.
[/Sources]

## Slide 8
Software remains—but the calculation stays in hardware
BUILD PLAN
JU RESEARCH • 32-BIT RISC-V • HARDWARE AI MATH ENGINE
08 / 8
SOFTWARE / RV32
• Compile equation into supported DFG / micro-ops
• Allocate buffers and write one job descriptor
• Configure solver, N, tolerances and limits
• Start the engine and handle result or fault
AI ENGINE HARDWARE
• Evaluate equation, gradient and Hessian
• Run factorization, solve, line search and update
• Repeat until convergence or bounded termination
• Store x*, metrics and a clear reason code
Recommended implementation order
1
Golden model
2
2-variable RTL
3
2-lane N-variable
4
AXI + RV32
5
NN integration
6
More solvers
Final result
A reusable hardware AI Engine IP: Newton is the first complete solver; future solvers reuse the dispatcher, memories, interfaces and arithmetic fabric.
Notes: Presenter notes:
- This is hardware-first rather than software-free: software owns setup and recovery; hardware owns every iterative calculation.
- Prove correctness with a bit-accurate model and a 2-variable RTL core before scaling the lane scheduler and AXI integration.
- Only after profiling should high-activity blocks be hardened into a custom macro or custom-designed arithmetic cells.
[Sources]
- User-provided JU project requirements and architecture discussion, 22 August 2026.
[/Sources]